## Slide 1
NICA Accelerator Complex :
Status, Problems, Perspectives
Igor Meshkov, Anatoly Sidorin and Grigory Trubnikov
for the NICA team
JINR, Dubna
31.10.2016
Hadronic Matter’2016

## Slide 2
Outline
Introduction: The NICA project at JINR
1. NICA @ Heavy Ion mode – Stages I & II of the project
2. NICA construction
3. Strategy of The Project Luminosity Achievement
4. Start up mode of the NICA operation
5. NICA – Stage III: Collider of polarized beams
6. Requirements and questions (to be discussed and answered)
Conclusion: the NICA beams

## Slide 3
NICA Collider basic parameters:
sNN = 4 - 11 GeV heavy ion colliding beams
at the luminosity L ~ 1027 cm-2 c-1 (Au)
and polarized p↑ (d↑) of sNN up to 26 (13) GeV at L ~ 1032 cm-2 c-1
is aimed at generation of intense heavy ion and polarized nuclear beams for searching the baryonic matter of a high density at modest temperature and investigation of polarization phenomena.
Introduction
The Nuclotron-based Ion Collider fAcility project at JINR

## Slide 4
Fixed Target Area
Nuclotron (45 Tm)
injection of one bunch
of  2×109 ions,
acceleration up to
1 - 4.5 GeV/u max.
Linac LU-20 (5MeV/u)
Ion sources
Booster (25 Tm)
1(2-3) single-turn injection,
storage of (2  4)×109 ions,
acceleration up to 100 MeV/u,
electron cooling, acceleration
up to 600 MeV/u
Linac HILac (3.2MeV/u)
ESIS KRION
1. NICA @ Heavy Ion mode
– 1st & 2nd Stages of The Project
Stripping (80%) 197Au31+ => 197Au79+
Two SC rings of the collider
NICA – Stage II
~ 2 x 22 injection cycles
22 bunches per ring
L ≥ 1027 см-2с-1
Baryonic Matter @ Nuclotron
BM@N: NICA – Stage I
s = 2.3 – 3.6 GeV/u (Au  Au)
MPD

## Slide 5
1. NICA @ Heavy Ion mode: 1st & 2nd Stages of The Project
In operation
Nucloron 0.6-4.5 GeV/u
MPD
Linac LU-20 (5 MeV/u)
Fixed target experiments
BM@N
Booster synchrotron
(600 MeV/u)
HILAc
(3 MeV/u)
Under construction
Electron cooler
(2.5 MeV)
SPD
C
o
l
l
i
d
e
r
1. NICA @ Heavy Ion mode
1st & 2nd Stages of The Project

## Slide 6
2. NICA construction
Status of The Nuclotron
Ion beams for fixed target: p, d, Li, C, Ar, Fe, … Xe
Nuclotron – 4.5 AGeV, 251 m.
superconducting synchrotron.
Commissioned in 1993,
Upgraded in 2011.
Adiabatic debunching and recapture at efficiency of about 95% was demonstrated

## Slide 7: Source for polarized particles (SPP) New injection complex of the NICA (Ion sources + HILAc) Heavy ion source: Krion-6T ESIS
B= 5.4T reached. Test Au beams produced:
- Au30+ ÷ Au3232+, 6*108, Tionization= 20 ms for
- Au31+ -> repetition rate 50 Hz.
- ion beams Au51+÷ Au54+ are produced.
Source had been commissioned,
achieved 1010 deutrons pp.
First beam run in June 2016
Heavy Ion Linear Accelerator under commissioning at JINR.
2. NICA construction

## Slide 8
Max. B field = 2T
Ramp rate – up to 4 T/s @ 1 Hz
two-phase LHe @ 4.5K
“Nuclotron-type”
SC hollow cable
Superconducting superferric “Dubna magnets”
2. NICA construction
The Magnet Plant
Booster dipole
Booster
quadrupole lens
Collider
“twin” dipoles

## Slide 9
2.3 m
4.0 m
Prototype of the Booster dipole
The best method to measure phase space size
V. Veksler
2.4 m
4.0 m
NICA Booster synchrotron
2. NICA construction

## Slide 10
BM@N and MPD
2. NICA construction
Baryonic Matter @ Nuclotron
(BM@N)
The fixed target experiment
at the Nuclotron - NICA Stage I
2017 – start
Au  Au
sNN = 2.3 – 3.6 GeV/u
MultiPurpose Detector
(MPD)
The collider experiment
at NICA Stage II
2020 - start up mode

## Slide 11
BM@N and MPD
2. NICA construction
Baryonic Matter @ Nuclotron
(BM@N)
June 2016:
Tests & commissioning at the Nuclotron beam subdetector located inside analyzing magnet
MPD superconducting Solenoid:
ASG superconducting (Genova, Italy):
Cold Mass + Cryostat, Vacuum System
Trim Coils
Control System & Power Supplies
General responsibility
B0 = 0.66 T , B/B ≤ 1e-4 in TPC area
Weight ~ 900 t
Vitkovice Heavy Machinery, Sept. 5, 2016
Control Dewar & pipe lines
Cryostat
SC coil
Trim Coil
Solenoid yoke
MultiPurpose Detector (MPD)

## Slide 12
Preproduction ECAL prototypes: co-operation with Ukraine and China
RPC deam test at NUCLOTRON: cooperation with SPb, China
TPC Cylinder C3 manufactured in Dec’13
RPC performance : required efficiency, rate capability & time resolution (63 ps) had been reached
ZDC coverage confirmed: 2.2<|h|< 4.8
FFD tested with beam: achieved time resolution (38 ps) is better than required
Readout Electronics developed for TPC, TOF, and ECAL (64 ch,13-bit,65 MSPS)
The CBM - MPD consortium: development & production of STS for CBM (FAIR), MPD & BM@N
mock-up carbon-fiber ladder (15 g / 1m)
Fabrication of MPD Subdetectors

## Slide 13
Construction of The Collider Building
2. NICA construction
October 28, 2016 Collider site

## Slide 14
2. NICA construction
NICA Collaboration
Budker INP:
Booster RF system, e-cooler
Collider RF systems
HV e-cooler for collider
Channel Nuclotron-Collider (?)
IHEP, Protvino
Beam dynamics,
Feed-back systems
Alikhanov ITEP
Beam dynamics, RFQ linac for LU-20
INP RAS, Troitsk:
Polarised ion source,
Beam diagnostics
iThemba Labs & 6 others (RSA)
Elements of the NICA accelerators
GSI/FAIR
SC magnets for
Booster/Collider/SIS-100,
UHV, beam cooling, diagnostics
FZ Juelich (IKP)
HV Electron cooler
Stochastic cooling
BNL (RHIC)
Beam dynamics,
Stochastic cooling
Fermilab
HV Electron cooler
Beam dynamics, stoch. cooling
CERN
SC and magnet technologies,
Rad.safety, energetics,
Beam cooling and dynamics,
Metrology
MEPhI, ARITP (Snezhinsk):
RFQ linac for LU-20
[HeliumMash, CryogenMash (Moscow)]

## Slide 15
3. Strategy of The Project Luminosity Achievement
Maximum r.m.s. bunch length is chosen equal to 0.6 m to have the “luminosity concentration” at Inner Tracker (IT) of MPD.
2. Maximum peak luminosity (limited by the beam space charge – the Lasslett tune shift) is achieved at maximum emittance:
Erms = 1.1 mmmrad (the beam radius = 1/6 of the ring aperture).
3. Maximum ion number per bunch is limited by
the tune shift value  0.05.
4. Number of bunches = 22 => to avoid parasitic collisions of the bunches in the common part of the Collider straight section.
5. RF multiplicity = 3 => separatrix area is by 25 times exceeds the beam longitudinal emittance.
6. The ratio between horizontal, vertical emittances and ion momentum spread is defined by the equilibrium of IBS rates for each degree of freedom.

## Slide 16
Parameter | Achieved |  | Project (2017 - 2020) | 
Magnetic field, T | 2.0 |  | 2.0 (B = 42.8 Tm) | 
Field ramp, T/s | 0.8 |  | 1.0 | 
Repetition period, s | 8.0 |  | 5.0 | 
 | E, GeV/u | Ions/cycle | Energy, GeV/u | Ions/ cycle
Light ions  d | 5.8 | 21010 | 6.0 | 51010
Heavy ions | With KRION-2 |  | With KRION-6T & Booster | 
40Ar18+ | 3.5 | 5106 | 4.9 | 1108 21010
56Fe26+ | 2.5 | 2106 | 5.4 | 1108 11010
124Xe48/42+ | 1.5 | 1103 | 4.0 | 1107 2109
197Au79+ | --- | --- | 4.5 | 1107 2109
Polarized beams | With Polaris |  | With SPI | 
p | --- | --- | 11.9 | 11010 **)
d | 2.0 | 5108 | 5.6 | 11010
**) With the Siberian snake and upgraded RF systems
3. Strategy of The Project Luminosity Achievement
Nuclotron Beams
NICA Stage II
With KRION-6T & Booster
**)

## Slide 17
Circumference, m | 503.04 |  | 
Number of bunches | 22 |  | 
rms bunch length, m | 0.6 |  | 
β-function in IP, m | 0.35 |  | 
Betatron tunes, Qx/Qy | 9.44 / 9.44 |  | 
Chromaticities, Q’x/Q’y | -33 / -28 |  | 
Ring Acceptance, π mm·mrad | 40 |  | 
Momentum acceptance, Δp/p | ±0.010 |  | 
γtr | 7.088 |  | 
Kinetic energy of Au79+, GeV/u | 1.0 | 3.0 | 4.5
Number of ions per bunch | 2.0·108 | 2.4·109 | 2.3·109
Δp/prms, 10-3 | 0.55 | 1.15 | 1.5
εrms, (h/v) π mm·mrad | 1.1/0.95 | 1.1/0.85 | 1.1/0.75
Luminosity, cm-2 s-1 | 0.6·1025 | 1·1027 | 1·1027
IBS growth time, s | 160 | 460 | 1800
Tune shift, Qtotal =QSC +2ξ | -0.050 | -0.037 | -0.011
The NICA Collider
Collider lattice:
FODO,
12 cells x 900
each arc
3. Strategy of The Project Luminosity Achievement

## Slide 18
3. Strategy of The Project Luminosity Achievement
RF Gymnastics in The Collider
VRF & ion bunches ,
arb. units
Step 1: Cooling and stacking with RF1 barrier voltage (< 5 kV). Accumulation efficiency ~ 95%, about 110 - 120 injection pulses (55-60 to each ring) every 5 sec. Total accumulation time ~ 10 min. Ion momentum spread is limited by microwave instability.
Steps 2-3. Formation of the short ion bunches at presence of cooling:
RF-2 (100 kV, 4 resonators) => RF-3 (1MV, 8 resonators).
From coasting beam to => 22nd harmonics => 66th harmonics
Phase, arb. units

## Slide 19
IBS dominated regime:
Stochastic cooling
to supress beam
Expansion IBS
SC dominated regime:
Electron cooling is
used to provide optimum
phase volume.
Effective stacking
with E-Cooling
3. Strategy of The Project Luminosity Achievement
Two modes of the collider operation
Space charge dominated mode (ΔQ ≤ 0.05) | IBS dominated mode
ε and dP/P are optimized independently. The bunch relaxation is suppressed by cooling. Luminosity is limited by space charge effects | ε and dP/P are “equi-partitioned”, either fast bunch relaxation. Luminosity can be obtained at small ΔQ<0.05

## Slide 20
3. Strategy of The Project Luminosity Achievement
Two modes of the collider operation
1 2 3 4
Ion energy, GeV/u
1.2
(Ei)
0.8
0.4
0
opt
Equilibrium beam emittance vs Eion , mmmrad
10
L(Ei)
1e27 cm-2s-1
1.0
0.1
0.01
1 2 3 4
Ion energy, GeV/u
Space charge IBS
dominated mode dominated
mode
Lopt
Nopt
10
Ion/bunch,
1E9
1.0
0.1
0.01
Nmax
Nopt
Lmax
Lopt
max
Electron and stochastic cooling application!
Emittance reduction with energy:
opt
Maximum of the Collider luminosity Lopt is limited
by the MPD counting rate!

## Slide 21
3. Strategy of The Project Luminosity Achievement
Strategy to keep Average Luminosity
Effective scheme of particle accumulation and bunch formation
Beam lifetime (if limited by scattering on residual atoms) ~ 10 h
“Head-tail” and multibunch instabilities are suppressed
by the feed-back systems.
4. Emittance growth due to IBS – suppressed by the beam cooling,
both electron and stochastic ones:
Ekin = 1 – 3 GeV/u – with electron cooling only,
Ekin = 3 – 4.5 GeV/u – with 3D stochastic and electron cooling.

## Slide 22
4. Start up mode of NICA operation
The beginning of the NICA accelerator complex commissioning
is scheduled for 2020
The complex will be commissioned with
- Injectors chain
- Transfer channels
- Collider in start up version, i.e:
with RF-1 and RF-2, but without RF-3
with Stoch. Coolg system - one channel per ring (long. cooling)
without Electron Cooler
without feed-back system
It will allow us to provide collider operation in the energy range of
sNN = 4 - 6 GeV ( 197Au79+ ions)
at the luminosity of
Lstart ≤ 5x1025 cm-2s-1

## Slide 23
5. NICA – Stage III: Collider of polarized beams
Polarization Control
Polarization
Control
2-nd Solenoid SS
1-st Solenoid SS
SPD
MPD
Spin diagnostics + Superconducting solenoids at field < 8 T
One of very preliminary versions -
to be analyzed and developed.
Spin Physics Detector (SPD)

## Slide 24
6. Requirements and questions (to be discussed and answered)
6.1. Choice of colliding nuclei
197Au79+  197Au79+ - main project option
197Au79+  p – main candidate for asymmetric collision mode
The questions:
Are these options optimal ?
Are the following symmetric colliding nuclei modes of the interest:
238U92+  238U92+, 208Pb82+  208Pb82+, 209Bi83+  209Bi83+, 131Xe54+  131Xe54+ ?
Are the following asymmetric collision modes of the interest:
197Au79+  d (, 7Li3+, 12C6+,…) ?
Replacing protons by the light ions (even deuteron!) simplifies significantly the Collider modifications for an asymmetric colliding nuclei mode.
6.2. Energy scan
a) What should be desirable energy step ?
b) What should be a precision, reproducibility and stability of
the chosen energy value ?
c) Do we need energy asymmetry of the colliding nuclei ?

## Slide 25
-100 -50 0 50 100
s [cm]
1.0
0.8
0.6
0.4
0.2
0
Local luminosity vs s
normalized by
project luminosity
dL/ds at s = 0 and
β* = 35 cm, s = 60 cm)
βmin = 35, 60, 100 cm
s = 60 cm
Inner Tracker of MPD
β* = 35, 60, 100 cm , s = 60 cm
Integral luminosity vs s
normalized by
project luminosity L at
β* = 35 cm, s = 60 cm)
9010 mm
6. Requirements and questions (to be discussed and answered)
6.3. Luminosity
a) Choice of the betatron function value in the interaction point (IP) – so called *
The increase of * leads to reduction of the luminosity (can be compensated (!), for instance, by increase of nuclei number), but allows one to resolve the problems of the Collider focusing systems!
The question: how does it influence on MPD characteristics ?

## Slide 26
6. Requirements and questions (to be discussed and answered)
6.3. Luminosity
b) MPD – what are upper and lower limits of counting rates (luminosity) ?
The upper level is known: 7 kHz. Can it be increased ?
The lower level – which (minimal) level of luminosity is of experiment interest ?
c) How absolute calibration of the luminosity can be performed at MPD ?
Usual method of calibration assumes measurement of the flux of small-angle
scattering particles in the collider. Is it foreseen at MPD ?
6.4. Collider and MPD synchronization
Traditional method of synchronization is control of the phase of rotating bunches in the ring. It allows one to tune the bunch rotation frequency and optimize the collision regime. The signal from collider control system can be used as a trigger allowing to “open” or “close” registration of reaction species and to measure background level. Such a system is under development by collider team and it’s time to coordinate common afforts.

## Slide 27
Concluding remarks:
NICA complex has a potential for competitive research
in dense baryonic matter and spin physics.
NICA has large international and fruitful cooperation with
many physics research centers in Russia and around
the World .
- The construction of the NICA collider complex and both
detectors BM@N & MPD goes close to the schedule.
We welcome new partners !
Thank you for your attention!

## Slide 28
Back up slides

## Slide 29
NICA time-line
 | 2015 |  |  |  | 2016 |  |  |  | 2017 |  |  |  | 2018 |  |  |  | 2019 |  |  |  | 2020 |  |  |  | 2021 |  |  |  | 2022 |  |  |  | 2023 |  |  | 
Injection complex |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Lu-20 upgrade |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
HI Source |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
HI Linac |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Nuclotron |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
general development |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
extracted channels |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Booster |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Collider |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
startup configuration |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
design configuration |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
BM@N |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I stage |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
II stage |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MPD |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
solenoid |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TPC, TOF, Ecal (barrel) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
upgraded end-caps |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Civil engineering |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MPD Hall |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SPD Hall |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
collider tunnel |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
HEBT Nuclotron-collider |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Cryogenic |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
for Booster |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
for Collider |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
running time

## Slide 30
6. Requirements and questions (to be discussed and answered)
running time
1) какой уровень светимости "уже интересен"?
MPD – upper and lower limits of counting rates (luminosity)
2) как влияет "длинная" светимость на работу MPD, т.е. dL/ds?
3) асимметричный режим - нужны ли протоны, или можно обойтись лёгкими ионами?
4) скан по энергии - диапазон, шаг, статистика на каждой точке энергии, воспроизводимость режимов?
5) Выбор сталкивающихся частиц –
А) сорт ядер
Б) асимметрия по массе – лёгкие х тяжёлые
6) Нужна ли симметрия по энергии?
What optimal step energy scan @ NICA could be expected?
What are optimal heavy ion species for collision? (U x U, or Au x Au, or Pb x Pb, or Bi x Bi, or Xe x Xe, similar or asimmetrical or isobars, p/d x HI, LI x HI)…
Minimal required detector space @ IP along the beam
Required modes of data acquisition (limitations, cycle, etc), collimation of the beam, requirements to the background “dead-time of detector”, requirements to the synchronization, are fragments from the pereferical collisions interesting ?
…. (to be cntd by weeknd)